## Slide 1
HD TVI IR PTZ Camera
1/3” 2.0 Mega-Pixel Panasonic CMOS Sensor
X360 Zoom Control (Optical X30 / Digital X12)
Digital Noise Reduction (2D+3D)
Day & Night with ICR (IR Cut Filter)
Digital Image Stabilizer
Intelligent IR LED Control
Minimum Illuminance 0.5 Lux (Color, DSS Off) / 0 Lux (IR Mode)
Endless 360° Endless Pan Rotation / Preset Speed 240°/sec.
The Shortest Path with Vector Drive Technology
Micro Control (0.05°/sec.) with Micro Stepping Control Technology
8 Privacy Masks with Spherical Coordinates
209 Presets / 10 Swings / 8 Patterns / 8 Groups
Built-in Wiper System [Option]
Approved IP67, IK10
Magnesium Material Body Case
Night Scout TVI (30X HD-TVI IR PTZ)
2.0M
X360 ZOOM
D&N (ICR)
0.5 LUX
0 LUX
VECTOR
MOTION
MICRO STEP CONTROL
TVI
&
COMPOSITE
ON-SCREEN
DISPLAY
ABC
PRIVACY MASK 8
M
M
360˚
ENDLESS
HDcctv V1.0
1.485Gb/s
SMPTE 292M
PRESET 209
1
2
3
4
SWING 10
1
2
PATTERN 8
GROUP 8
1
2
3
RTC &
SCHEDULER 8
VANDAL-
PROOF
WEATHER
PROOF
IP67
ALARM
3 IN / 2 OUT

## Slide 2
Specifications
www.cynix.co.kr
Category |  | (NTSC for Composite Output) | (PAL for Composite Output)
Camera | Image Sensor | 1/3'' Panasonic Progressive Scan CMOS Sensor | 
 | Resolution | 2,000K pixels | 
 | Zoom | 30X Optical Zoom, 12X Digital Zoom | 
 | Focal Length | F1.4~4.6, f=4.4~132.0mm | 
 | Video Signal to Noise | 50 dB | 
 | Angle of View | 62.9° (Wide)~2.2° (Tele) | 
 | Min. Working Distance | 100mm(Wide), 1,000mm(Tele) | 
 | Focus Control | Auto / Manual / Semi-Auto / Interval AF | 
 | AE Mode | Auto / Iris / Shutter / Manual / Brightness | 
 | White Balance | Auto / Indoor / Outdoor / Manual (Red, Blue Gain Adjustable) | 
 | Day & Night | Auto / Day / Night (ICR) | 
 | Minimum Illuminance | 0.5 Lux (Color, DSS Off) / 0 Lux (IR Mode) | 
 | BLC | On / Off | 
 | WDR | On / Off | 
 | Defog | Off / Low / Mid / High | 
 | Aperture | Adjustable | 
 | NR (Noise Reduction) | Yes | 
 | Stabilization | Off / On | 
 | Privacy Zone | Off / On (8 Masks with Spherical Coordinate) | 
Infrared | IR Range | 250m | 
 | Brightness Control | Auto (Proportional to Zoom) / Off / Manual (2~127 Steps) | 
 | IR Wave Length | 850nm | 
Pan/Tilt | Range | Pan : 360°(Endless) / Tilt : -20°~90° | 
 | Pan/Tilt Speed | Preset : 240° / sec. | 
 |  | Manual : 0.05° ~ 240° / sec. (Proportional to Zoom) | 
 |  | Swing : 10°~180° / sec. | 
 | Preset | 209 Presets (Label, Independent Camera Parameter Setting) | 
 | Pattern | 8 Patterns [768 Commands (Approximate 5 Minutes) / Pattern] | 
 | Swing | 10 Swings | 
 | Group | 8 Groups (MAX. 40 Actions with The Combination of Preset, Pattern and Swing) | 
 | Schedules | 8 Schedules | 
 | Other Functions | Auto Flip, Auto Parking, Power-up Action & etc. | 
Video | Output | HD TVI : 1920x1080p30/25, CVBS : 1Vp-p | 
 | OSD | English (Menu / Time / PTZ information etc. Password protection) | 
RTC(Real Time Clock) |  | Yes (RTC Battery Backup Time : Approximate 2 Weeks) | 
PTZ Control | Communication | RS-485 / UTC | 
 | Protocol | RS-485 : Pelco-D / Pelco-P, UTC : Pelco-C / Hikvision-C | 
Sensor / Alarm | Sensor Input | 3 Input, Photo-Coupler Type, DC 5V~12V | 
 | Alarm Output | 2 Output, Relay Output, MAX. Load DC 24V / 1.0A or AC 125V / 0.5A | 
Fan & Heater |  | Built-in | 
Physical | Mount Bracket | Wall Mount Bracket or Ceiling Mount Bracket | 
 | Dimension | Camera Body : 260(Ø) x 365(H) [mm] Wall : 410.5 x 471mm / Ceiling : 260(Ø) x 541.5mm | 
 | Weight | Approximate 7.6 kg | 
 | Rated Power | AC 24V 3A | 
 | Waterproof | IP 67 | 
 | Operating Temp. | -30°C ~ 50°C / 22°F ~ 122°F | 
 | Wiper | Built-in Wiper [Option] | 
# Specification & Design are subject to change without prior notice. |  |  |